AT-779UV

MOBILE RADIO

Specification

| General | Transmitting Part | Receiving Part |  |
| --- | --- | --- | --- |
| Frequency Range |  | VHF:136-174MHz |  | Wide band | Narrow band |  | Wide band | Narrow band |
|  |  | UHF:400~490MHz |  |  |  |  |  |  |
| Number of Channels |  | 500 Channels | Power Output | VHF: > 20W | Sensitivity | ≤0.25μV | ≤0.35μV |
|  |  |  |  | UHF: > 18W | (12dBm SINDA) |  |  |
| Channel Spacing |  | 25K (Wide Band) | Modulation | 16KΦF3E | 11KΦF3E | Adjacent Channel | ≥70dB | ≥60dB |
|  |  | 12.5K (Narrow band) |  |  |  | Selectivity |  |  |
|  | 2.5KHz,5KHz,6.25KHz,10KHz, | Adjacent Channel Power | ≥70dB | ≥60dB | Audio Response | +1~-3dB | +1~-3dB |
| Phase-locked Step | 12.5KHz,15KHz,20KHz,25KHz, |  |  |  |  |  |  |
|  |  |  |  |  |  | (0.3~3KHz) | (0.3~2.55KHz) |
|  | 30KHz,50KHz |  |  |  |  |  |  |
| Operating Voltage | DC 13.8V±15% (Ordinary version) | Hum & Noise | ≥40dB | ≥36dB | Hum & Noise | ≥45dB | ≥40dB |
|  | DC 12V~28V (Wide voltage version) |  |  |  |  |  |  |
| Squelch |  | Carrier /CTCSS/DCS/ | Spurious | ≥60dB | ≥60dB | Audio distortion |  | <3% |
|  |  | 5Tone/2Tone/DTMF | Emission |  |  |  |  |  |
| Frequency Stability |  | ±2.5ppm | Audio Response | +1~-3dB | +1~-3dB | Audio power output | >2W@10% |
|  |  |  |  | (0.3~3KHz) | (0.3~2.55KHz) |  |  |
| Operating |  | -20℃~+60℃ | Audio Distortion |  | ≤5% |  |  |  |
| Temperature |  |  |  |  |  |  |  |  |
| Dimensions |  | 124(W)x101(D)x36(H)mm |  |  |  |  |  |  |
| (WxDxH) |  |  |  |  |  |  |  |  |
| Weight |  | about 0.45kg |  |  |  |  |  |  |
| Standard Accessories |  |  |  |  |  |  |
|  |  | PPT |  |  |  |  |  |  |
| 779UVV/M |  |  |  |  |  |  |  |  |
| MIC |  |  |  |  |  |  |  |  |
| MAIN |  | VOL |  |  |  |  |  |  |
| MON | FUN |  |  |  |  |  |  |  |
| Transceiver | Microphone | Mobile Bracket | Spare Fuses | non-slip mat | Microphone Hanger |
|  |  |  | 5A 250V |  |  |

Adjusting screws	Pads	Tapping screws	User Manual

Optional Accessories

PC cable	External Speaker	Car Antenna

A1.200912

ISO 9001:14001

Tel: +7 495 235-7510

E-mail: anytone@anyradio.ru

Website: https://www.anyradio.ru https://www.anytone.su