Firmware Updating

1. Install USB driver: GD_VirtualComDriver ，

choose X86 for 32bit system, X64 for 64bit system.

(if you already intall the driver for PC cable, no need to install again)

2. Install QXCodePro_Update_dpinst_Setup_1.02.exe

3. Hold PTT key and alarm key, at the same time power on radio, the red LED blink.

4. Use the PC cable to connect PC and radio

5. Double Click QXCodePro_Update_dpinst_Setup_1.02.exe to run it

6. Click Open Update File，choose D268P_V101_20220628.spi

7. Choose correct Com Port

8. Click Write to update the radio the latest firmware.

9. Reboot the radio Main Control Unit (MCU) when the update is finished. See below:

Rebooting the MCU

After updating the firmware, you need to reset to the radio Main Control Unit (MCU). Power off the radio first. Then power it on while holding the PTT and the PF1 button below the PTT at the same time.

*** Please Wait – and do not turn the radio off while it restarts *** After the MCU reboot, you will have to set the time and date. Use the P1 key to scroll through the date / time fields. Up and Down arrow keys will allow you to change the information in these fields. After you have the information entered use the Green key to confirm the settings.