V10	TWO WAY RADIO

Specification

Frequency Range

Channel Number

Channel Spacing

Phase-locked Step

Operating Voltage

Frequency Stability

Operating Temperature

Size

General

RX	TX

136-174MHz(Asian version)

144-146MHz(European version)

136-174MHz	144-148MHz(USA version)

400-480MHz	400-480MHz(Asian version)

430-440MHz(European version)

430-450MHz(USA version)

16 Channels

25KHz (Wide Band)

12.5KHz (Narrow Band)

5KHz, 6.25KHz

7.4V DC ±20%

±2.5ppm

-20℃~ +55℃

59x118x36mm ( with 1200mAh battery)

| Transmitting Part | Receiving Part |
| --- | --- |
| Power Output | ≤5W | Sensitivity | ≤0.25μV (Wide Band) |
|  |  | (12dB SINAD) | ≤0.35μV (Narrow Band) |
| Modulation | 16KΦF3E (Wide Band) | Adjacent Channel | ≥70dB (Wide Band) |
|  | 11KΦF3E (Narrow Band) | Selectivity | ≥60dB (Narrow Band) |
| Adjacent Channel | ≥70dB (Wide Band) | Inter-modulation | ≥60dB (Wide Band) |
| Power | ≥60dB (Narrow Band) |  | ≥60dB (Narrow Band) |
| Hum & Noise | ≥45dB (Wide Band) | Spurious Rejection | ≥65dB (Wide Band) |
|  | ≥40dB (Narrow Band) |  | ≥65dB (Narrow Band) |
| Spurious Emission | ≤-36dB (Wide Band) | Hum & Noise | ≥45dB (Wide Band) |
|  | ≤-36dB (Narrow Band) |  | ≥40dB (Narrow Band) |
|  | +1~-3dB(0.3~3KHz) |  | +1~-3dB(0.3~3KHz) |
| Audio Response | (Wide Band) | Audio Response | (Wide Band) |
|  | +1~-3dB(0.3~2.55KHz) |  | +1~-3dB(0.3~2.55KHz) |
|  | (Narrow Band) |  | (Narrow Band) |
| Audio Distortion | ≤5% | Audio Distortion | ≤5% |  |
|  |  | Audio Power Output | 1000mW/10% |

| Weight | 203g( with 1200mAh battery) |
| --- | --- |

Standard Accessories

17cm Antenna	Li-Ion Battery	Charger	Belt Clip	User Manual

(1200mAh)

Optional Accessories

|  | USB Programming | Hand Strap | Earpiece | Li-Ion Battery Pack | 10cm Antenna | 40cm Antenna |
| --- | --- | --- | --- | --- | --- | --- |
|  | Cable |  |  | (2600mAh) |  |  |

A1.200813

ISO 9001:14001

ISO 9001:14001

Tel: +7 495 235-7510

E-mail: anytone@anyradio.ru

Website: https://www.anyradio.ru https://www.anytone.su